## Slide 1: LabB Presentation Bloom Filter
Speaker：Chang Shu (r09943161)
Advisor：Prof. Jiin Lai
Date：2022.10.27

## Slide 2: Outline
Bloom filter
  Introduction
  Run on CPU (baseline)
Partition among CPU and FPGA
Object
Improving skills
  Multi-kernel
  Multi-buffer
  Multi-DDR
Conclusion

## Slide 3: Bloom Filter
Check whether an element is present in the dataset
Use a hash table-based data structure
  space efficient
  reduces the number of database queries
query returns
  possibly in a set(False-positive matches are possible)
  definitely not in set

## Slide 4: Bloom Filter
The colored arrows show each set element map to bit array
The element w is not in the set {x, y, z}
  hashes to a one bit-array position containing 0

## Slide 5: Bloom Filter
Consist of two parts
  Compute hash function
  Compute score
Computing hash value takes 1458.8ms (84.5% of total run time)
Computing score takes 268.5ms (15.5% of total run time)

## Slide 6: Partition among CPU and FPGA
The compute of the hash for a single word ID consists of:
  4 XORs
  3 arithmetic shifts
  2 multiplication
The 3 arithmetic operations
Shift 44-bits totally when
len = 3
  requires 44 cycles on CPU
  requires 3 cycles on FPGA

## Slide 7: Partition among CPU and FPGA
One word is independent of other words
  Unroll
Accesses to the “input_doc_words” array sequentially
  Access DDR in burst mode
Run on FPGA

## Slide 8: Partition among CPU and FPGA
takes only about 15.5% of the total running time
  Provide little performance benefit
Memory Access depend on the “word_id”
  Access DDR randomly in non-burst mode
Run on host CPU

## Slide 9: Object
FPGA Processing
  Write DDR (1400 MB/9.5 GBps = ~147 ms)
  Compute Hash
  Read DDR (350 MB/12 GBps = ~30 ms)
Host CPU Processing
  Compute Score (268.5 ms)
Write DDR
Compute Hash
Read DDR
Compute Score
FPGA Processing
CPU Processing

## Slide 10: Object
Should be executed in pipeline
  Latency of the Compute on FPGA will become invisible
Maximum Throughput
  Min(write DDR, Compute on FPGA, read DDR, Compute on CPU)

## Slide 11: Object
Overlap processing time
  Write DDR
  Compute Hash
  Read DDR
  Compute Score
Improving technique
  Multi-kernel
  Multi-buffer (batch splitting)
  Multi-DDR
Write DDR
Compute Hash
Read DDR
Compute Score
FPGA Processing
CPU Processing

## Slide 12: Multi-Kernel
Process multiple words every clock cycle
  Ex. # of kernel is 4,8,16……
PARALLELISATION = 4
# of Kernel = 4
Compute 4 words in parallel

## Slide 13: Multi-Kernel
4x Kernel
8x Kernel
Process more multiple words every clock cycle achieve less FPGA compute time

## Slide 14: Multi-Kernel
Write DDR
Compute Hash
Read DDR
Compute Score
FPGA Processing
CPU Processing
Write DDR
Compute Hash
Read DDR
Compute Score
FPGA Processing
CPU Processing

## Slide 15: Data bandwidth
Reading 16 words per DDR access
  DDR bandwidth / word size = 512bits / 32bits = 16
Unroll = 4
  Send 128 bits for 4 words to process in parallel
DDR
512 bits
Buffer
32bits
Resize
512 bits
32bits
32bits
32bits
FPGA

## Slide 16: Data bandwidth
Reading 16 words per DDR access
  DDR bandwidth / word size = 512bits / 32bits = 16
Unroll = 8
  Send 256 bits for 8 words to process in parallel
DDR
512 bits
Buffer
Resize
512 bits
32bits
FPGA
32bits
32bits
32bits
32bits
32bits
32bits
32bits

## Slide 17: Multi-Buffer
Timeline And Performance
2x Buffer + 8x Kernel

## Slide 18: Multi-Buffer
Overlap of data transfer and compute on FPGA with split buffers
  Split the documents and send them to the FPGA in two iterations
  The kernel can start the compute as soon as the data for the corresponding iteration is transferred to the FPGA.

## Slide 19: Multi-Buffer
Overlap of data transfer and compute on FPGA with split buffers
  Split the documents and send them to the FPGA in two iterations
  The kernel can start the compute as soon as the data for the corresponding iteration is transferred to the FPGA.
  Exist boundary for Kernel parallelisation
Write DDR
Compute Hash
Read DDR
Compute Score
FPGA Processing
CPU Processing
Write DDR
Compute Hash
Read DDR

## Slide 20: Multi-Buffer
Overlap of host data transfer and compute with multiple buffers
  Splitting the documents into 2, 4, 8, 16, 32 and 64 chunks
  Exist boundary
Chart: FPGA execution time vs Number of iteration
| 1 | 2 | 4 | 8 | 16 | 32 | 64
number of iteration | 575 | 502 | 463 | 450 | 446 | 448 | 447

## Slide 21: Multi-Buffer
Timeline And Performance
8x Buffer + 8x Kernel

## Slide 22: Multi-Buffer
Overlap data transfer from host, compute on FPGA and profile score on the CPU
  Enables the host to start profile scores as soon as the flags are received
Check if flags processed by FPGA is greater than needed by CPU. Else, block CPU

## Slide 23: Multi-Buffer
Overlap data transfer from host, compute on FPGA and profile score on the CPU
  Enables the host to start profile scores as soon as the flags are received
Write DDR
Compute Hash
Read DDR
Compute Score
FPGA Processing
CPU Processing
Write DDR
Compute Hash
Read DDR
Write DDR
Compute Hash
Write DDR

## Slide 24: Multi-Buffer
Timeline And Performance
8x Buffer + 8x Kernel

## Slide 25: Multi-DDR
Use multiple banks in ping-pong fashion to minimize the contention
  CPU write DDR bank1, FPGA read DDR bank2
  CPU write DDR bank2, FPGA read DDR bank1
  CPU&FPGA can access DDR at the same time
input word is set to array of sub-buffers created from buffer_doc_words[0] and buffer_doc_words[1] alternatively; hence, data is sent to DDR bank 1 and 2 alternatively in each kernel execution

## Slide 26: Multi-DDR
Use multiple banks in ping-pong fashion to minimize the contention
  CPU write DDR bank1, FPGA read DDR bank2
  CPU write DDR bank2, FPGA read DDR bank1
  CPU&FPGA can access DDR at the same time
Write DDR
Compute Hash
Read DDR
Compute Score
FPGA Processing
Write DDR
Compute Hash
Read DDR
Write DDR
Compute Hash
Write DDR

## Slide 27: Conclusion
Performance
  Throughput improved form 0.81Gbs to 4.22Gbs
  Achieve faster computing speed
  Overlap Processing time
Technique Applied
  Pipeline
  Parallelisation
  Ping-pong buffer

## Slide 28: Thank You