## Slide 1: LabA: Host Code Optimization
Speaker: Edan
Advisor: Prof. Jiin Lai
Date: 2022/10/20

## Slide 2: Performance Optimization of HLS
Host program optimization
  Schedule the tasks to increase the u-rate of kernels
Kernel code optimization
  Pipeline/parallelize the kernel
Topological optimization
  Connect a specific DDR to a specific kernel
Implementation optimization
  DSP or LUT for the kernel
We will focus on the host program optimization

## Slide 3: System Diagram
read: convert AXI to AXI_Stream
write: convert AXI_Stream to AXI
exec: add processDelays to the input and write out the result after processDelays cycles

## Slide 4: Used Pragma
PIPELINE
  Reduces the II into 1 as possible
  Depends on the read and write latency
    How many copies of HW required
DATAFLOW
  Enable task-level pipelining
  Especially for adjacent for loops
  Also reduce the II of the entire function
  Not working in current example
    Shown in the result

## Slide 5: Code of Module-pass
read
write
exec
pass_dataflow

## Slide 6: Host Program
Flow chart
ApiHandle
  Setup device
  Create kernel
  Create queue
Task
  Create global buffer for input and output
  Set kernel args
  Move input data to global buffer
  Start kernel
  Read output data from the global buffer

## Slide 7: Current Settings
numBuffers
  Total number of tasks
  Set to 10 in the first and 100 in the second task
oooQueue
  Set the queue as the out-of-order queue
  Set to true except the first experiment of Lab1
processDelay
  The number required to be added to the output
  Set to 1
bufferSize
  The number of input data per task
  Set as 16384 in the first two labs and sweep in the third lab

## Slide 8: Lab1: Use the In-order Queue
Setup params
Execution code

## Slide 9: Lab1: Use the In-order Queue
Timeline
Total execution time: 0.043s

## Slide 10: Lab1: Use the Out-of-order Queue
Setup params
Execution code

## Slide 11: Lab1: Use the In-order Queue
Timeline
Total execution time: 0.043s → 0.024s

## Slide 12: Observation
The execution of one pass is longer in oooqueue
  Longer latency per task
Problem in the current design
  No synchronization until the end
  If the numBuffers is too large → FPGA will consume too much host memories, which can only be released at the end of the program.

## Slide 13: Lab2: Kernel and Host Code Synchronization
OpenCL framework has two methods for synchronization
  clFinish and clWaitForEvents
Modify the execution section

## Slide 14: Lab2: Kernel and Host Code Synchronization
Timeline
Total execution time: 0.024s → 0.033s

## Slide 15: Observation
It is like a trade-off between in-order-queue and out-of-order queue
  Out-of-order inside a batch, in-order between batches
The clFinish is the synchronization point of the host program
  Called four times in Lab2

## Slide 16: Lab2: Kernel and Host Code Synchronization
We can let the current task depends on the finish of the previous task
Execution code

## Slide 17: Lab2: Kernel and Host Code Synchronization
Timeline
Total execution time: 0.033s → 0.027s
  More overlap reduce execution time

## Slide 18: Lab2: Kernel and Host Code Synchronization
Using clWaitForEvent
Timeline

## Slide 19: Lab3: OpenCL API Buffer Size
Set numBuffer to 100 to get a more accurate average throughput estimate per transfer
We then sweep the buffer size from 214 to 221 to observe the change of the throughput
Saturate when buffer size is close to 220
The saturated throughput is approximate 34000Mb/s

## Slide 20: Summary
Host code indeed influences the execution time and resource usage
  Good host code make your kernel highly utilized without occupy too many host resources
The final sweep of the buffer size indicates the proper buffer size to use in our system to make the interface fully utilized

## Slide 21: Q&A
How to release the buffer occupied by the host code?
  Insert clFinish
  Insert clWaitForEvent
  Let event depends on the finish of the previous event