## Slide 1: High Accuracy Image Classifier Inference on PYNQ-Z2
Team8
b07901073吳秉軒 r11943012曾維雋 r11943043潘奕亘
Graduate Institute of Electronics Engineering
National Taiwan University
Dec 29th, 2022

## Slide 2: Outline
Goal
Training setting
Immigrate to QNN, onnx
Model selection
Software issue
FINN implementation
Conclusion
Reference

## Slide 3: Outline
Goal
Training setting
Immigrate to QNN, onnx
Model selection
Software issue
FINN implementation
Conclusion
Reference

## Slide 4: Goal
Image classifier on cifar10 using ResNet
Implement 2 version:
  1. Lightweight ResNet based on baseline accuracy (~85%)
  2. Maximize the utilization of resources on PYNQ-Z2 (or KV260) to approach best performance (~90%)
Design a methodology of tuning model’s parameter
(Option) Finish an End-to-end image classifier application accelerated with FPGA

## Slide 5: Training set
Start from ResNet18
Preprocessing
  RandomCrop
  RandomHorizontalFlip
  Normalize
Optimizer: SGD
  Learning rate: 0.1, momentum: 0.9, weight decay: 5*10-4
  Scheduler: CosineAnnealingLR
Epoch: 200
Batch size: 128

## Slide 6: Immigrate to QNN
Using layer from QNN library
  QuantIdentity for input and shortcut
  Conv2d -> QuantConv2d
  Set bit width for each layer’s parameters
Export with FINNManager
  onnx file

## Slide 7: Outline
Goal
Training setting
Immigrate to QNN, onnx
Model selection
  Lightweight model
  Max-utilized model
Software issue
FINN implementation
Conclusion
Reference

## Slide 8: Model selection
Parameter setting
  Layer
  Channel
  Bit width
Design 2 versions
  Light-weight model (~85%)
  Max-utilized model (~90%)

## Slide 9: Original model
Model: Resnet18-4w4a
Accuracy: 92.54%
Total parameter: 11,164,352
Layer | Num of Param
Conv0 | 1,728
Group1 | 147,456
Group2 | 524,288
Group3 | 2,097,152
Group4 | 8,388,608
Fully-connected | 5,120

## Slide 10: Observation
Last block of ResNet18
  Take about 75% of model’s parameters
Duplicand of ResNet block
  2 for each ResNet block in ResNet18
ResNet8
  Remove last block & 1 duplicand
  Little impact on accuracy
    92.54% -> 90.11%
  Large impact on resources (onnx file)
    ~44000kB -> ~4900kB

## Slide 11: Observation
Search on channel & bit width
  Channel: 8~64
  Bit width: 4~8
Conclusion
  Suitable number of layer (for a specific accuracy)
  Adjust channel and bit width
    Impact: channel > bit width

## Slide 12: Light-weight model
Model: Resnet8-6w6a
Accuracy: 84.51% (↓8.03%)
Total parameter: 77,360 (↓ 99%)
16
16, /2
16
32
32
64
64
16*16
8*8
4*4
Layer | Num of Param | Decreased %
Conv0 | 432 | 75%
Group1 | 4,608 | 97%
Group2 | 14,336 | 97%
Group3 | 57,344 | 97%
Group4 | 0 | 100%
Fully-connected | 640 | 87%

## Slide 13: Max-utilized model
Maximize the utilization to get higher accuracy (~90%)
  Truncate the model to fit in the PYNQ-Z2
    Reduce layer
    Reduce channel
  Maximize the resource
    Slightly increase channels
    Slightly increase bit width
  Approach ideal accuracy

## Slide 14: Resnet10
Model: Resnet10-4w4a
Accuracy: 91.57%
Total parameter: 4,897,472
Layer | Num of Param
Conv0 | 1,728
Group1 | 73,728
Group2 | 229,376
Group3 | 917,504
Group4 | 3,670,016
Fully-connected | 5,120

## Slide 15: Resnet8
Model: Resnet8-4w4a
Accuracy: 89.98%
Total parameter: 1,224,896 (↓ 75%)
Layer | Num of Param
Conv0 | 1,728
Group1 | 73,728
Group2 | 229,376
Group3 | 917,504
Fully-connected | 2,560

## Slide 16: Reduce half of the channel
Model: Resnet8-4w4a
Accuracy: 87.63%
Total parameter: 307,296 (↓ 75%)
Layer | Num of Param | Decreased %
Conv0 | 864 | 50%
Group1 | 18,432 | 75%
Group2 | 57,344 | 75%
Group3 | 229,376 | 75%
Fully-connected | 1280 | 50%

## Slide 17: Increase channel
Model: Resnet8-4w4a
Best accuracy
  Increase number of channel of the last group
  Accuracy: 88.5% (↑0.87%)
Version | Conv0 | Group1 | Group2 | Group3 | FC | Acc %
Base | 32 | 32 | 64 | 128 | 10 | 87.63
First group | 48 | 48 | 64 | 128 | 10 | 88.09
Middle group | 32 | 32 | 96 | 128 | 10 | 87.85
Last group | 32 | 32 | 64 | 144 | 10 | 88.5

## Slide 18: Increase bit width
Model: Resnet8-5w5a
Best accuracy
  5 bits for all layers
  Accuracy: 89.33% (↑1.7%)
Version | Conv0 | Group1 | Group2 | Group3 | FC | Acc %
All 4b | 4 | 4 | 4 | 4 | 4 | 87.63
First + last | 5 | 4 | 4 | 4 | 5 | 88.23
Middle | 4 | 5 | 5 | 5 | 4 | 88.15
All 5b | 5 | 5 | 5 | 5 | 5 | 89.33

## Slide 19: Software issue
onnx generation
  Should use QuantIdentity for shortcut
  Should put model on CPU before export
onnx size
  Only represent resource of parameter
  Synthesize result also involve architecture

## Slide 20: Outline
Goal
Training setting
Immigrate to QNN, onnx
Model selection
Software issue
FINN implementation
  Transform
  Issue
  Result
Conclusion
Reference

## Slide 21: Difference of Architecture
VGG
  Convolution
  Max pooling
ResNet
  Convolution
  Max pooling
  Short-cut path
  Average pooling

## Slide 22: FINN Transform
Input ONNX
Tidy Up
Streamlined
Dataflow
Folded
Hardware Generation
ResNet-dependent flow
  Tackle with the operations of Resnet
  Quantized Neural Network
Accelerate the transform flow
More flexible for testing

## Slide 23: FINN Transform
Input ONNX
Tidy Up
Streamlined
Dataflow
Folded
Hardware Generation
Linear streamline
  Similar to VGG’s flow
Non-linear streamline
  Short-cut path
  MoveLinearPastEltwiseAdd()

## Slide 24: FINN Transform
Input ONNX
Tidy Up
Streamlined
Dataflow
Folded
Hardware Generation
BNN
  InferBinaryMatrixVectorActivation()
  InferQuantizedMatrixVectorActivation()
QNN
  InferQuantizedMatrixVectorActivation()

## Slide 25: FINN Transform
Input ONNX
Tidy Up
Streamlined
Dataflow
Folded
Hardware Generation
Folded parameter setting
  Configure PE, SIMD and FIFO
There are some constraints
  SIMD must divide IFMChannels
  MatrixVectorActivaton requires SIMD >= MW/1024
  FIFO depth doesn’t have big effect on resource utilization

## Slide 26: FINN Issue
Input ONNX
Tidy Up
Streamlined
Dataflow
Folded
Hardware Generation
Assertion error
  Signed output requires actval < 0
Solution
  AbsorbSignBiasIntoMultiThreshold()
  Add it to the beginning of Streamlined
  Absorb signed int bias into MultiThreshold and re-evaluate the output type.
Notes: There is a transformation missing at the beginning of the streamlining block, which is the absorb. AbsorbSignBiasIntoMultiThreshold() transformation. This transformation would normally set the out_bias attributes accordingly.

## Slide 27: FINN Issue
Input ONNX
Tidy Up
Streamlined
Dataflow
Folded
Hardware Generation
Folded output shape is not consistent
  Fpgadataflow.InsertDWC()
  Fpgadataflow.InsertFIFO()
Eliminate these commands
  DWC(data width converter) may cause error.

## Slide 28: Implementation Result
High accuracy version (ResNet10, 90.11%)
Layer | W bit | Shape | Channel
Conv0 | 4 | 32x32 | 3
Conv1_0 | 4 | 32x32 | 64
Conv1_1 | 4 | 16x16 | 64
Conv1_2 | 4 | 32x32 | 64
Conv2_0 | 4 | 16x16 | 64
Conv2_1 | 4 | 16x16 | 128
Conv2_2 | 4 | 8x8 | 64
Conv3_0 | 4 | 16x16 | 128
Conv3_1 | 4 | 4x4 | 256
Conv3_2 | 4 | 8x8 | 128
Element | ResNet10 |  | PYNQ-Z2
LUT | 64463 | 121% | 53200
LUTRAM | 6630 | 38% | 17400
FF (slice) | 96921 | 91% | 106400
BRAM | 178 | 127% | 140
BUFG | 1 | 3% | 32

## Slide 29: Implementation Result
High accuracy version (ResNet8, 89.33%)
Layer | W bit | Shape | Channel
Conv0 | 5 | 32x32 | 3
Conv1_0 | 5 | 32x32 | 32
Conv1_1 | 5 | 32x32 | 32
Conv2_0 | 5 | 32x32 | 32
Conv2_1 | 5 | 16x16 | 64
Conv2_2 | 5 | 32x32 | 32
Conv3_0 | 5 | 16x16 | 64
Conv3_1 | 5 | 8x8 | 128
Conv3_2 | 5 | 16x16 | 64
Element | ResNet8 |  | PYNQ-Z2
LUT | 40593 | 76% | 53200
LUTRAM | 3150 | 18% | 17400
FF (slice) | 63355 | 60% | 106400
BRAM | 76 | 54% | 140
BUFG | 1 | 3% | 32

## Slide 30: Implementation Result
Lightweight version (ResNet10, 84.51%)
Layer | W bit | Shape | Channel
Conv0 | 6 | 32x32 | 3
Conv1_0 | 6 | 32x32 | 16
Conv1_1 | 6 | 16x16 | 16
Conv1_2 | 6 | 32x32 | 64
Conv2_0 | 6 | 16x16 | 16
Conv2_1 | 6 | 8x8 | 32
Conv2_2 | 6 | 16x16 | 16
Conv3_0 | 6 | 8x8 | 32
Conv3_1 | 6 | 4x4 | 64
Conv3_2 | 6 | 8x8 | 32
Element | ResNet10 |  | PYNQ-Z2
LUT | 35617 | 67% | 53200
LUTRAM | 2707 | 15% | 17400
FF (slice) | 46435 | 44% | 106400
BRAM | 29 | 21% | 140
BUFG | 1 | 3% | 32

## Slide 31: Conclusion
Model truncation
  Critical layer: last convolution layer
  Impact: channel > bit width
Parameter suggestion (for PYNQ-Z2)
  Layer: ~10
  Bit width: 4-6 bits
FINN implementation
  Model-dependent transform
  At most 80% HW utilization
Performance | Accuracy | Lightweight
LUT | 76% | 67%
LUTRAM | 18% | 15%
FF (slice) | 60% | 44%
BRAM | 54% | 21%
BUFG | 3% | 3%
Accuracy | 89.33% | 84.51%

## Slide 32: Reference
https://github.com/Xilinx/brevitas
https://xilinx.github.io/finn/
https://finn.readthedocs.io/en/latest/source_code/finn.transformation.fpgadataflow.html