## Slide 1: High Accuracy Image Classifier Inference on PYNQ-Z2
Team 8
B07901073 吳秉軒 R11943012 曾維雋 R11943043 潘奕亘
Advisor: Professor Lai-Jin
Dec 8th, 2022

## Slide 2: Outline
Problem Statement
Project Scope
Project Plan

## Slide 3: Outline
Problem Statement
Project Scope
Project Plan

## Slide 4: Image Classifier
Image classification has been widely used in many applications, such as medicine image, face recognition, and defect detection
CNN has demonstrated excellent results in computer vision tasks
Model
  VGG introduces deep CNN with small kernel
  ResNet resolves gradient vanishing and uses deeper CNN

## Slide 5: Model Selection
Dataset
  Start from relatively small dataset (e.g., cifar10)
VGG vs. ResNet
  Top-5 accuracy on ImageNet
    VGG16: 92.3%
    ResNet152: 95.51%
  Top-1 [1]
Ref: An Analysis of Deep Neural Network Models for Practical Applications, 2016

## Slide 6: Model Selection
Model analysis
  Comparison between VGG and ResNet
  Using same size of models: VGG5 and ResNet10
  Result: ResNet achieve better accuracy (70% vs. 81%)
Model setting
  ResNet10
  Adam optimizer (learning rate: 0.001)
  Batch size: 16

## Slide 7: Objective
Implement 2 version:
  1. Lightweight ResNet based on baseline accuracy
  2. Maximize the utilization of resources on PYNQ-Z2 (or KV260) to approach best performance
Design a methodology of tuning model’s parameter
(option)Finish an End-to-end image classifier application accelerated with FPGA

## Slide 8: Outline
Problem Statement
Project Scope
Project Plan

## Slide 9: Software
Image preprocessing
  RGB to grayscale
  Data augmentation (e.g., ColorJitter, RandomFlip)
Layer reduction
  Fit large model into PYNQ
Bit precision of intermediate layers
  Tradeoff between accuracy and resources
Methodology of tuning
  Several factors: # of layer, size & bit width of each layer
  Record the increase of resource and accuracy
  Follow the trend
  More during the process …

## Slide 10: Operation Flow
Host
  Generate data
  Preprocessing
  Accuracy result
Kernel
  Inference computing
  Dataflow – FIFO depth
  Folding factor

## Slide 11: Target
Throughput
  [2] achieved 21.9 kFPS with 80.1% accuracy for the binary weight VGG on ZC706
Accuracy (on cifar10)
  Resnet-50: 98.3%
  VGG-19: 94.71%
Achieve compatible throughput by lightweight model on Resnet with acceptable accuracy
Maximize the utilization of resources on PYNQ-Z2 (or KV260) to approach the accuracy of 90%

## Slide 12: Outline
Problem Statement
Project Scope
Project Plan

## Slide 13: Workflow
Implement & improve Pytorch code on Brevitas (1 – 1.5w)
  Data preprocessing
  Scaling model
FINN implementation & performance analysis
  Throughput
  Accuracy
  Layer-by-layer resource usage
  Testing
Vitis-HLS analysis
  Resource utilization

## Slide 14: reference
[1] Canziani, A., Adam Paszke and Eugenio Culurciello. “An Analysis of Deep Neural Network Models for Practical Applications.” ArXiv abs/1605.07678 (2016): n. pag.
[2] Y. Umuroglu, N. J. Fraser, G. Gambardella, M. Blott, P. Leong, M. Jahre, and K. Vissers, ‘‘FINN: A framework for fast, scalable binarized neural network inference,’’ in Proc. ACM/SIGDA Int. Symp. Field-Program. Gate Arrays, Feb. 2017, pp. 65–74