## Slide 1: LabB: Systolic Array
Speaker: Edan
Advisor: Prof. Jiin Lai
Date: 2022/10/27

## Slide 2: Systolic Array
Applications
  Solving linear systems: QR-decomposition
  DNN inferencing: TPU
Advantages
  Reduce time complexity
    From O(n3) to O(n) in QRD
Modules
  Processing element
    Multiply-and-accumulate
    Rotations
  PE array

## Slide 3: Overall System in LabB
Matrix multiplication with systolic array
  localA: MAX_SIZE*MAX_SIZE
  localB: MAX_SIZE*MAX_SIZE
  localC: MAX_SIZE*MAX_SIZE
  localC = localA*localB
Systolic array in this lab
  PE array with size of MAX_SIZE*MAX_SIZE
  Output stationary manner
    Move both arrays and accumulate the output in the same PE

## Slide 4: Kernel Code

## Slide 5: Using 3x3 Matrices to Illustrate
Pragma
  localA, localB, localC
    Array partition: shown in red line
  Systolic1
    Unroll: create 9 PEs to work in parallel
Every item in c uses 3 cycles to accumulate the result
  Output stationary
Every element in localA and localB are broadcasted

## Slide 6: Broadcast Mechanism
Every PE accumulates the partial sum from the inner product of two vectors.
Array partitioned can be explained as turn an array into vectors

## Slide 7: From Code to Time Sequence (1/6)
readA, readB

## Slide 8: From Code to Time Sequence (2/6)
Mux
  Can be optimized

## Slide 9: From Code to Time Sequence (3/6)
Multiplication

## Slide 10: From Code to Time Sequence (4/6)
Load last value

## Slide 11: From Code to Time Sequence (5/6)
Accumulate

## Slide 12: From Code to Time Sequence (6/6)
Write back

## Slide 13: Timeline Analysis (1/2)
w/ array partition
Kernel time: 47.83us

## Slide 14: Timeline Analysis (2/2)
w/o array partition
Kernel time: 76.824us

## Slide 15: Time and Resource Analysis (1/2)
With array partition

## Slide 16: Time and Resource Analysis (2/2) **
w/o array partition

## Slide 17: Generated Verilog Code (1/2)
w/ array partition
Generate several rams for partitioned arrays (vectors)

## Slide 18: Generated Verilog Code (1/2)
w/ array partition
Several addresses and data channel for pipeline readA, readB, writeC

## Slide 19: Generated Verilog Code (1/2)
w/o array partition
Only one address and data channel for pipeline readA, readB, writeC

## Slide 20: Summary
In this example, w/ and w/o array partition takes almost the same latency
  w/ array partition, it uses the FF to store the arrays
  w/o array partition, it uses the FF and BRAM to store the arrays
Although no pipeline pragma, the readA, readB, writeC are automatically pipelined
  Optimized by HLS

## Slide 21: BUT!!!

## Slide 22: A Real Systolic Array
The aforementioned implementation is not a real systolic array
  No communications between PEs
A real systolic array example for matrix multiplication [1]

## Slide 23: Example Mentioned on the LabB-note
Non-stationary Systolic Array (NSA) Design [2]
Only difference
  C is exported in left sequentially
  C is directly exported from the systolic array in right

## Slide 24: Code for Real SA
A: 6x6
B: 6x6
C: 6x6
SA: 3x3
Register in SA
SA Init
Tiling
Tiling
Propagating in SA
Input new values from the original array
Parallel calculation and accumulation

## Slide 25: Tiling
A
B
C
*
SA
=

## Slide 26: Operation in One Tile
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
r=0
Shift
A
B
A00
0
0
A01
A10
0
A02
A11
A20
…
…
…
B00
B10
B20
B01
B11
B02
0
0
0
…
…
…
C

## Slide 27: Operation in One Tile
A00 | 0 | 0
0 | 0 | 0
0 | 0 | 0
B00 | 0 | 0
0 | 0 | 0
0 | 0 | 0
r=0
Input
A
B
A01
0
A02
A11
A03
A12
A21
…
…
…
B10
B20
B30
B11
B21
B12
0
…
…
…
A10
A20
B01
B02
C

## Slide 28: Operation in One Tile
A00 | 0 | 0
0 | 0 | 0
0 | 0 | 0
B00 | 0 | 0
0 | 0 | 0
0 | 0 | 0
r=0
Cal.
A
B
A01
0
A02
A11
A03
A12
A21
…
…
…
B10
B20
B30
B11
B21
B12
0
…
…
…
A10
A20
B01
B02
A00*B00 |  | 
C

## Slide 29: Operation in One Tile
0 | A00 | 0
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
B00 | 0 | 0
0 | 0 | 0
r=1
Shift
A
B
A01
0
A02
A11
A03
A12
A21
…
…
…
B10
B20
B30
B11
B21
B12
0
…
…
…
A10
A20
B01
B02
A00*B00 |  | 
C

## Slide 30: Operation in One Tile
A01 | A00 | 0
A10 | 0 | 0
0 | 0 | 0
B10 | B01 | 0
B00 | 0 | 0
0 | 0 | 0
r=1
Input
A
B
A02
A03
A12
A04
A13
A22
…
…
…
B20
B30
B40
B21
B31
B22
…
…
…
A11
A21
B11
B12
A20
B02
A00*B00 |  | 
C

## Slide 31: Operation in One Tile
A01 | A00 | 0
A10 | 0 | 0
0 | 0 | 0
B10 | B01 | 0
B00 | 0 | 0
0 | 0 | 0
r=1
Cal.
A
B
A02
A03
A12
A04
A13
A22
…
…
…
B20
B30
B40
B21
B31
B22
…
…
…
A11
A21
B11
B12
A20
B02
A00*B00+A01*B10 | A00*B01 | 
A10*B00 |  | 
C

## Slide 32: Operation in One Tile
0 | A01 | A00
0 | A10 | 0
0 | 0 | 0
0 | 0 | 0
B10 | B01 | 0
B00 | 0 | 0
r=2
Shift
A
B
A02
A03
A12
A04
A13
A22
…
…
…
B20
B30
B40
B21
B31
B22
…
…
…
A11
A21
B11
B12
A20
B02
A00*B00+A01*B10 | A00*B01 | 
A10*B00 |  | 
C

## Slide 33: Operation in One Tile
A02 | A01 | A00
A11 | A10 | 0
A20 | 0 | 0
B20 | B11 | B02
B10 | B01 | 0
B00 | 0 | 0
r=2
Input
A
B
A03
A04
A13
A05
A14
A23
…
…
…
B30
B40
B50
B31
B41
B32
…
…
…
A12
A22
B21
B22
A21
B12
A00*B00+A01*B10 | A00*B01 | 
A10*B00 |  | 
C

## Slide 34: Operation in One Tile
A02 | A01 | A00
A11 | A10 | 0
A20 | 0 | 0
B20 | B11 | B02
B10 | B01 | 0
B00 | 0 | 0
r=2
Cal.
A
B
A03
A04
A13
A05
A14
A23
…
…
…
B30
B40
B50
B31
B41
B32
…
…
…
A12
A22
B21
B22
A21
B12
A00*B00+A01*B10+ A02*B20 | A00*B01+A01*B11 | A00*B02
A10*B00+A11*B10 |  | 
A20*B00 |  | 
C

## Slide 35: Operation in One Tile
……

## Slide 36: Operation in One Tile
0 | 0 | 0
0 | 0 | 0
0 | 0 | A25
0 | 0 | 0
0 | 0 | 0
0 | 0 | B25
r=9
Shift
A
B
A00*B00+A01*B10+ A02*B20+A03*B30+ A04*B40+A05*B50 | A00*B01+A01*B11+ A02*B21+A03*B31+ A04*B41+A05*B51 | A00*B02+A01*B12+ A02*B22+A03*B32+ A04*B42+A05*B52
A10*B00+A11*B10+ A12*B20+A13*B30+ A14*B40+A15*B50 | A10*B01+A11*B11+ A12*B21+A13*B31+ A14*B41+A15*B51 | A10*B02+A11*B12+ A12*B22+A13*B32+ A14*B42+A15*B52
A20*B00+A21*B10+ A22*B20+A23*B30+ A24*B40+A25*B50 | A20*B01+A21*B11+ A22*B21+A23*B31+ A24*B41+A25*B51 | A20*B02+A21*B12+ A22*B22+A23*B32+ A24*B42
C

## Slide 37: Operation in One Tile
0 | 0 | 0
0 | 0 | 0
0 | 0 | A25
0 | 0 | 0
0 | 0 | 0
0 | 0 | B25
r=9
Input
A
B
A00*B00+A01*B10+ A02*B20+A03*B30+ A04*B40+A05*B50 | A00*B01+A01*B11+ A02*B21+A03*B31+ A04*B41+A05*B51 | A00*B02+A01*B12+ A02*B22+A03*B32+ A04*B42+A05*B52
A10*B00+A11*B10+ A12*B20+A13*B30+ A14*B40+A15*B50 | A10*B01+A11*B11+ A12*B21+A13*B31+ A14*B41+A15*B51 | A10*B02+A11*B12+ A12*B22+A13*B32+ A14*B42+A15*B52
A20*B00+A21*B10+ A22*B20+A23*B30+ A24*B40+A25*B50 | A20*B01+A21*B11+ A22*B21+A23*B31+ A24*B41+A25*B51 | A20*B02+A21*B12+ A22*B22+A23*B32+ A24*B42
C

## Slide 38: Operation in One Tile
0 | 0 | 0
0 | 0 | 0
0 | 0 | A25
0 | 0 | 0
0 | 0 | 0
0 | 0 | B25
r=9
Cal.
A
B
A00*B00+A01*B10+ A02*B20+A03*B30+ A04*B40+A05*B50 | A00*B01+A01*B11+ A02*B21+A03*B31+ A04*B41+A05*B51 | A00*B02+A01*B12+ A02*B22+A03*B32+ A04*B42+A05*B52
A10*B00+A11*B10+ A12*B20+A13*B30+ A14*B40+A15*B50 | A10*B01+A11*B11+ A12*B21+A13*B31+ A14*B41+A15*B51 | A10*B02+A11*B12+ A12*B22+A13*B32+ A14*B42+A15*B52
A20*B00+A21*B10+ A22*B20+A23*B30+ A24*B40+A25*B50 | A20*B01+A21*B11+ A22*B21+A23*B31+ A24*B41+A25*B51 | A20*B02+A21*B12+ A22*B22+A23*B32+ A24*B42+A25*B52
C

## Slide 39: Timeline Analysis
Kernel time: 84.414us
47.83 -> 84.414

## Slide 40: Time and Resource Analysis
Latency of SA
  21 -> 51
LUT
  40k -> 33k
FF
  63k -> 78k

## Slide 41: Summary
Total cycles per tile
  N+2M-2
Why not ok?
  A complicate mux
Real SA vs Not Real SA
  Not Real SA
    Require only 3 cycles per tile -> latency is shorter
    High routing resource due to broadcasting -> larger LUT usage
  Real SA
    Require 7 cycles per tile -> longer latency
    Use additional registers for propagations between PEs -> Larger FF usage

## Slide 42: Q&A
In the NSA design, if all matrix size are 5, and the size of the SA is also 5. Using the real SA design, how many cycles we need to finish one tile?
  13

## Slide 43: Reference
[1] https://www.telesens.co/2018/07/30/systolic-architectures/
[2] Asgari, Bahar, Ramyad Hadidi, and Hyesoon Kim. "Meissa: Multiplying matrices efficiently in a scalable systolic architecture." 2020 IEEE 38th International Conference on Computer Design (ICCD). IEEE, 2020.