## Slide 1: Fast Object Detection from Point Clouds for Autonomous Driving
T1: 陳奕達 戴妤珊 蔡岳峰
Advisor: Prof. Lai-Jiin
Date: 2022/12/29

## Slide 2: Outline
Background
Model
Executing on GPU
Executing with Vitis AI
Executing with FINN
Comparison
Conclusion

## Slide 3: Background

## Slide 4: Background
Why object detection in autonomous driving
  Vehicle detection
  Pedestrian detection
  Cyclist detection
LiDAR (3D point cloud) vs Cameras
  More detail and accurate distances
  More complex data to be processed

## Slide 5: Motivation of Accelerating Object Detection in Autonomous Driving
In autonomous driving, the system requires continuing monitoring the driving environment.
Real time processing is required
  Latency
  Throughput

## Slide 6: Dataset – KITTI Vision Benchmark Suite [1]
Provided data (#: 7481)
  Point clouds from the LiDAR sensor
  Images from four cameras (two monochrome and two color)
  Information from the GPS/IMU navigation system

## Slide 7: Model

## Slide 8: Target Model: PointPillars [2]
Modules
  Pillar Feature Network (PFN): convert point cloud to a pseudo-image
  Backbone: PointNet
  SSD Detection Head
Lower complexity: 2D conv vs 3D conv

## Slide 9: Backbone: PointNet CVPR’ 17
Point cloud classification
  Mainly compose of CNN and MLP

## Slide 10: Model in PyTorch

## Slide 11: Executing on GPU

## Slide 12: PointPillars on GPU
NVIDIA RTX A5000
 | NVIDIA RTX A5000
Energy consumption (W) | 171
Frames per second | 54.45

## Slide 13: Executing with vitis AI

## Slide 14: Measuring Environment
ZCU104
  PYNQ: 85K logic, 220 DSP
  KV260: 256K logic, 1.2K DSP
OS
  PetaLinux
Power meter
  Measure total power of ZCU104 for calculating power efficiency

## Slide 15: Vitis-AI: PointPillars Overview
Execution flow of Vitis-AI
  System flow is accelerated by PL (DPU)
  325MHz on DPU, 650MHz on DSP, 2048 MACs
ZCU 104
PS (Linux)
PL
Lidar data reader
Data preprocessing
Pillar Feature Net
Scatter operation
Backbone & Detection Head
Postprocessing
PC
Data output

## Slide 16: Vitis-AI: PointPillars Implementation
Vitis-AI is highly wrapped by API library
  Pseudo code of Vitis-AI PointPillars model
Create nets for PointPillars
  Including PointNet and Region Proposal Network (RPN)
Read point cloud data
Run the inference of the net

## Slide 17: Vitis-AI: PointPillars Results (1/2)
Average inference time in Vitis-AI: 18.472 FPS
  End-to-end time: 54.028ms
  DPU execution time: 33.853ms

## Slide 18: Vitis-AI: PointPillars Results (2/2)
Power consumption
-
= 1.9w

## Slide 19: Executing with FINN

## Slide 20: FINN: PointPillars Overview
Execution flow of FINN
  Only backbone and SSD are accelerated on PL
  HW: pp.xclbin, model: pipline.config
Github link:https://github.com/vision-agh/pp-finn

## Slide 21: FINN: PointPillars Results (1/2)
We discover that the FINN version is modified from Vitis AI repo
  The environment and the makefiles are too complicated
Reproduce results
Run time comparison (vs. paper)
  Voxelization: 7.13m → 84m (14x)
  Extend feature vector: 1.65m → 140m (84x)
  PFN: 62.43m → 1683m (26x)
  scatter: 0.72m → 1.24m (1.7x)
  Pre: 3.1m → 5.6m (1.8x)

## Slide 22: FINN: PointPillars Results (2/2)
Power consumption estimation
-
= 0.2w

## Slide 23: Model Transplant
As reported in the paper, the FPS is 2.67
  The modified backbone may be the root cause
The modified backbone is transplant to the Vitis AI to evaluate its FPS
  Vitis AI reported 5.41 FPS
  Almost 4x slower
We can conclude that the modification of the original model for the FINN has large impact on FPS

## Slide 24: Comparison

## Slide 25: Visualization Analysis (1/3)
GPU
Vitis AI
Vitis AI and GPU end up with similar results

## Slide 26: Visualization Analysis (2/3)
GPU
Vitis AI
Vitis AI and GPU end up with similar results

## Slide 27: Visualization Analysis (3/3)
GPU
Vitis AI
Vitis AI lose information in some cases

## Slide 28: Comparison Table
 | GPU | Vitis AI | FINN
Device | RTX A5000 | ZCU104 | ZCU104
FPS | 54.45 | 18.472 | 2.67
Power (watt) | 171 | 1.9 | 0.2
Frame per Joule | 0.32 | 9.722 (30x) | 13.35 (41.74x)

## Slide 29: Conclusion
FPGAs still shows superior energy efficiency compared with GPUs
Develop with both Vitis AI and FINN is much difficult than PyTorch/CUDA
Vitis AI
  Easier to deploy
  No space to finetune
  Only for application development
FINN
  Requires several tools to generate the final executable files
  Trade-off: model complexity vs. model compatibility
    Generalizability vs. efficiency
Hard to debug → segmentation fault …
Compatibility between different versions
  Difficult to setup the environment

## Slide 30: Reference
[1] Geiger, A., Lenz, P., Stiller, C., & Urtasun, R. (2013). Vision meets robotics: The KITTI dataset. International Journal of Robotics Research (IJRR).
[2] Lang, Alex H., et al. "Pointpillars: Fast encoders for object detection from point clouds." Proceedings of the IEEE/CVF conference on computer vision and pattern recognition. 2019.