## Slide 1
High Level Synthesis
Nov 3, 2022
Presenter: Yi-Chen Chu
Advisor: Prof. Jiin Lai​
Graduate Institute of Electronics Engineering, National Taiwan University
LabB: Discrete Fourier Transform (DFT)

## Slide 2: DFT Algorithm
DFT
Real
Image

## Slide 3: DFT-256 Software Implementation
Possible improvement
  Sin, Cos lookup table
  Storage minimization
  Pipeline II = 1
Initialization
Two Loop
Calculation
In-place
DFT

## Slide 4: DFT-256 Direct-mapped Design
Performance
  Inner pipeline loop: 50 + 5 * 256 = 1330
  Outer loop: 256 * 1334 = 341504
Two II violation
Memory Dependency, II=5
Resource Limitation, II=2

## Slide 5: Cosine, Sine Lookup Table
From DFT
  Look up table

## Slide 6: Storage Minimization
Separate I/O ports -> reduce two BRAM

## Slide 7: Pipeline II = 1
Use different m_axi adapter
  No resource limitation
Loop interchange
  No memory dependence
#pragma HLS PIPELINE II = 1

## Slide 8: DFT-256 Optimization
Performance
  342285 cycles -> 73480 cycles
Utilizations and instances

## Slide 9: Comparison and Conclusion
Comparison Table
Conclusion
  By using pipeline method, process time can be reduced by 4.65x.
  By loop interchange and more m_axi adapter, II violation can be solved.
 |  | Direct-mapped | This work
Process Time (cycles) |  | 342285 | 73480
I/O ports |  | 2 | 4
m_axi Adapter |  | 1 | 4
Hardware Resource | BRAM | 2 (Data buffer) | 2 (cos, sin coefficient buffer)
 | DSP | 14 | 20
 | FF | 5151 | 5671
 | LUT | 6558 | 9246

## Slide 10: Questions
How to calculate loop latency?
Loop latency = Iteration latency + (N - 1) * Initiation Interval
What is “bundle” in #pragma HLS INTERFACE mode=m_axi port=in bundle=gem_0
Groups function arguments into AXI interface ports.