## Slide 1: LabB Cholesky Factorization
Speaker: Chi-Tse Huang
Adiviser: Prof. Jiin Lai
Date: 2022/10/26

## Slide 2: Outline
Introduction to Cholesky Factorization
Vitis HLS
  Baseline
  Pipeline
  Pipeline – II = 1
  Datatype
  Unroll
Vitis Runtime

## Slide 3: Introduction to Cholesky Factorization
Decomposition of a Hermitian, positive-definite matrix
  the product of a lower triangular matrix and its conjugate transpose.
Application
  Monte Carlo simulations

## Slide 4: Cholesky Algorithm
Serial time complexity is
The storage for matrix A and L can share
The j-th column of L only need the columns ahead
  The computing order of column can not be changed
  The entry in the same column can be computed parallelly
Matrix A
Matrix L
Sharing
Stage | Dimension | 16 | 32 | 64 | 128 | 256 | 512
CPU code | Run Time (CPU) | 1us | 3us | 25us | 195sus | 1694us | 16013us

## Slide 5: Baseline
Read Data
Cal First Col
Cal Cols
Write Data

## Slide 6: Pipeline -- II=7
Data dependency
  Create more buffer to separate the operations in the different loop
Read Data IL=3
Multiplication IL=8
Addition IL=8

## Slide 7: Pipeline – Buffer
Assign different times of loop to different buffers
  Break the data dependency
Use pipelined adder tree to calculate the final sum.
tmp0
Adder Tree
tmp
Buffer Size > Original II
 II should can be reduced to 1

## Slide 8: Pipeline – Buffer
Buffer Size = 8
Need at least 9 buffers to reduce II=1  16 buffers

## Slide 9: Pipeline – II=2 / II=1
Buffer Size = 8
Buffer Size = 16
Name | BRAM_18K | DSP | FF | LUT
DSP | 0 | 0 | 0 | 0
Expression | 0 | 0 | 0 | 298
FIFO | 0 | 0 | 0 | 0
Instance | 0 | 20 | 4041 | 4824
Memory | 32 | 0 | 0 | 0
Multiplexer | 0 | 0 | 0 | 1982
Register | 0 | 0 | 1183 | 0
Total | 32 | 20 | 5224 | 7104
Name | BRAM_18K | DSP | FF | LUT
DSP | 0 | 0 | 0 | 0
Expression | 0 | 0 | 0 | 298
FIFO | 0 | 0 | 0 | 0
Instance | 0 | 20 | 4041 | 4824
Memory | 32 | 0 | 0 | 0
Multiplexer | 0 | 0 | 0 | 1982
Register | 0 | 0 | 1183 | 0
Total | 32 | 20 | 5224 | 7104

## Slide 10: Comparison
When dimension=16, the overhead of pipelined adder tree is larger than the benefits.
As the dimension grows
  The benefit of pipelining is more significant
  Separating the loop into the 16 groups can make II=1
    More groups(>16) induce more overhead
Stage | Dimension | 16 | 32 | 64 | 128 | 256 | 512
CPU code | Run Time (CPU) | 1us | 3us | 25us | 195sus | 1694us | 16013us
Module1 Baseline Pipeline Off | Vitis EMU-HW (Kernel) | 75us | 434us | 3110us | 23477us |  | 
Module2 Pipeline | Vitis EMU-HW (kernel) | 53us | 241us | 1436us | 9826us |  | 
Module2 Pipeline Adder Tree=8 II=2 | Vitis EMU-HW (kernel) | 60us | 226us | 1010us | 5212us | 30204us | 
Module2 Pipeline Adder Tree=16 II=1 | Vitis EMU-HW (kernel) | 67us | 245us | 1059us | 4809us |  | 
-58%
-51%

## Slide 11: Datatype
Host program can tolerance some error
Convert the double variable to the float variable
  Reduce the precision
Error Tolerance

## Slide 12: Comparison
Name | BRAM_18K | DSP | FF | LUT | URAM
DSP | 0 | 0 | 0 | 0 | 0
Expression | 0 | 0 | 0 | 298 | 0
FIFO | 0 | 0 | 0 | 0 | 0
Instance | 0 | 14 | 2784 | 3406 | 0
Memory | 16 | 0 | 0 | 0 | 0
Multiplexer | 0 | 0 | 0 | 1663 | 0
Register | 0 | 0 | 996 | 0 | 0
Total | 16 | 14 | 3780 | 5367 | 0
Name | BRAM_18K | DSP | FF | LUT | URAM
DSP | 0 | 0 | 0 | 0 | 0
Expression | 0 | 0 | 0 | 298 | 0
FIFO | 0 | 0 | 0 | 0 | 0
Instance | 0 | 20 | 4041 | 4824 | 0
Memory | 32 | 0 | 0 | 0 | 0
Multiplexer | 0 | 0 | 0 | 1982 | 0
Register | 0 | 0 | 1183 | 0 | 0
Total | 32 | 20 | 5224 | 7104 | 0
Double
Float
Dimension | 16 | 32 | 64 | 128
Pipeline Off | 75us | 434us | 3110us | 23477us
Pipeline On II=7 | 53us | 241us | 1436us | 9826us
Dimension | 16 | 32 | 64 | 128
Pipeline Off | 60us | 285ns | 2094us | 15899us
Pipeline On II=7 | 43us | 198us | 1275us | 9113us

## Slide 13: Unroll -- Concept
Splits the matrix L to multiple tiles
Tile 0
Tile 1
Tile 2
Tile 3
The entries of the same col have no dependencies
Executed Simultaneously
Matrix L
NCU=2

## Slide 14: Unroll -- Code
Read Data
Write Data
Cholesky
Array Partition
Matrix A Cyclic Partition

## Slide 15: Unroll -- Core
Compute the diagonal entry and store row j
Compute the column entries
Data A has been partition
  dataj is to duplicate the j-th row data NCU times

## Slide 16: Unroll – chol_jj unit
Store the j-th row for other entries of the same column

## Slide 17: Unroll – chol_col
dataj need to store in advance

## Slide 18: Experimental Result
Stage | Dimension | 16 | 32 | 64 | 128 | 256 | 512
CPU code | Run Time (CPU) | 1us | 3us | 25us | 195sus | 1694us | 16013us
Baseline Pipeline Off | Vitis EMU-HW (Kernel) | 75us | 434us | 3110us | 23477us |  | 
Pipeline (II=7) | Vitis EMU-HW (kernel) | 53us | 241us | 1436us | 9826us |  | 
Pipeline Adder Tree=8 II=2 | Vitis EMU-HW (kernel) | 60us | 226us | 1010us | 5212us | 30204us | 
Pipeline Adder Tree=16 II=1 | Vitis EMU-HW (kernel) | 67us | 245us | 1059us | 4809us | 23925us | 
Unroll Factor=16 | Vitis EMU-HW (kernel) | 19us | 49us | 149us | 543us | 2283us | 
Unroll Factor=32 | Vitis EMU-HW (kernel) | 20us | 41us | 118us | 393us | 1537us | 
Unroll Factor=16 | Vitis HW (Run) | 138us | 152us | 304us | 812us | 2824us | 13004us
Unroll Factor=16 | Vitis HW (kernel) | 87us | 102us | 245us | 731us | 2716us | 12912us
After these optimizations, the runtime can be reduced under CPU